## Slide 1
Post-Fire Watershed Risk Portal
Satellite-Driven Debris Flow Triage for Emergency Response | Integrating Google Earth Engine with USGS Empirical Volume Modeling
Anthony Brandi | California Polytechnic State University, San Luis Obispo | CAFES Symposium, May 13, 2026
Cal Poly Logo
+ NRES Department
QR: Live App
Abstract
Post-fire debris flows are the leading secondary cause of wildfire fatalities in the western US. Current assessment methods require days of manual BAER field work — time that does not exist when atmospheric rivers follow within weeks of containment. The 2018 Thomas Fire / Montecito debris flow: 23 deaths, 5 weeks post-containment. This tool integrates Google Earth Engine satellite burn severity analysis with the USGS Gartner (2014) empirical volume model to rank-order watershed vulnerability within one hour of fire perimeter availability — replacing days of field assessment with a satellite-driven triage workflow.
The Model
ln(V) = 4.22 + 0.39*sqrt(i15) + 0.36*ln(Bmh) + 0.13*sqrt(R)
Gartner et al. (2014) | Engineering Geology, 176, 45-56
Variable | Definition
i15 | Peak 15-min rainfall intensity (mm/hr)
Bmh | Area burned at moderate-high severity (km2)
R | Watershed relief: max minus min elevation (m)
Three satellite inputs. One risk ranking.
Deliverable within one hour of containment.
Data pipeline: USGS SRTM 30m DEM + ESA Sentinel-2 SR 10m burn severity + USGS WBD HUC-12 watersheds, processed live in Google Earth Engine Python API.
Three satellite inputs. One risk ranking.
Deliverable within one hour of containment.
Operational Output
REPLACE: Thomas Fire choropleth map
Module 2 at 91 mm/hr
Fig. 1 -- HUC-12 basin predicted sediment yield, Thomas Fire (2017), recorded storm 91 mm/hr. Red = extreme risk.
Results — Validation Across Three Independent California Fires
Does the model rank basins correctly? Yes — Spearman rho > 0.89 across all three fires.
Grand Prix Fire (2003)
Spearman rho = 1.000 | n = 7 basins | Mean ratio = 1.09x
REPLACE: Grand Prix Fire (2003) rank chart
Rank-preservation -- sorted by observed volume
REPLACE: Grand Prix Fire (2003) ratio chart
Predicted/Observed ratio per basin
Fig. 2a -- Rank chart: gray bars = USGS observed, colored bars = Gartner predicted (blue=under, white=accurate, red=over). Fig. 2b -- Ratio dots: above dashed line = over-prediction, below = under-prediction. Best case: Perfect rank ordering. All 7 basins in correct risk sequence. Mean ratio 1.09x -- essentially unbiased. Gartner (2014) within its stated calibration domain.
Station Fire (2009)
Spearman rho = 0.895 | n = 20 basins | Mean ratio = 0.96x
REPLACE: Station Fire (2009) rank chart
Rank-preservation -- sorted by observed volume
REPLACE: Station Fire (2009) ratio chart
Predicted/Observed ratio per basin
Fig. 3a -- Rank chart: gray bars = USGS observed, colored bars = Gartner predicted (blue=under, white=accurate, red=over). Fig. 3b -- Ratio dots: above dashed line = over-prediction, below = under-prediction. Strong case: Largest sample (20 basins). Rank correlation p < 0.001. Mean ratio 0.96x -- unbiased once repeat storm events averaged per basin.
Thomas Fire (2018)
Spearman rho = 0.900 | n = 5 basins | Mean ratio = 1.71x at 24 mm/hr
REPLACE: Thomas Fire (2018) rank chart
Rank-preservation -- sorted by observed volume
REPLACE: Thomas Fire (2018) ratio chart
Predicted/Observed ratio per basin
Fig. 4a -- Rank chart: gray bars = USGS observed, colored bars = Gartner predicted (blue=under, white=accurate, red=over). Fig. 4b -- Ratio dots: above dashed line = over-prediction, below = under-prediction. Boundary case: Rank ordering correct (p = 0.037). Volumes over-predicted at 24 mm/hr design storm -- explained by storm input mismatch, not model failure. See right column.
Rank ordering is preserved across all three fires (rho > 0.89). The model correctly identifies highest-risk basins for evacuation triage even when absolute volume predictions are imperfect.
The Interpolation Penalty
Why does Thomas over-predict at 24 mm/hr?
REPLACE: Thomas gauge map
Blue = gauges. Orange = basins.
Line opacity = interpolation distance.
Fig. 5 -- Single ALERT gauge serving five Thomas Fire basins. Faded lines = high spatial interpolation of i15.
Storm Input Comparison
Storm input | Mean ratio
Design storm (24 mm/hr) | 1.71x over-predicted
Recorded storm (91 mm/hr) | ~1.05x near-accurate
The model structure is correct. It needs accurate storm input.
Key Takeaways
Triage accuracy holds. Spearman rho > 0.89 across three independent fires. The model correctly rank-orders basin vulnerability for evacuation prioritization even with imperfect rainfall data.
The interpolation penalty is real. Absolute volume error scales with gauge-to-basin distance. Rank ordering is robust. Volume magnitude accuracy requires co-located rain gauges.
Operational speed. Full basin-level risk assessment in under one hour of fire perimeter availability -- versus days for traditional BAER field assessment.
Future work. Sourcing ALERT gauge coordinates for Grand Prix (2003) and Station (2009) from San Bernardino Co. and LA County DPW will quantify the interpolation penalty empirically across all fires.
Data: Crowder et al. (2025) USGS doi:10.5066/P13EZSWW | Model: Gartner et al. (2014) Engineering Geology 176:45-56 | Satellite: ESA Sentinel-2 SR + USGS SRTM via Google Earth Engine